## Slide 1
HEAT ENGINE & Combustion of biodiesels part 7
Notes: Source: ap06/p1/thermal/ptG_engines.ppt

## Slide 2: Today’s objectives:
To verify energy content of various fuels.
To compare regular diesel to biodiesel.
To explain how a diesel fuel engine work.
To understand the Otto cycle and apply its process to heat exchanges.
To calculate the efficiency of various engines.
To explain how a 4 stroke engine process work.

## Slide 3
Part 1:
Carnot
Heat Engines

## Slide 4
Heat engine: device that transforms heat partly into work (mechanical energy) by a working substance undergoing a cyclic process.

## Slide 5
petrol engine: fuel + air

## Slide 6
All heat engines absorb heat QH from a source at a relatively high temperature (hot reservoir TH), perform some work W and reject some heat QC at a lower temperature (cold reservoir TC).
 Qnet = |QH| - |QC| = W
Example of a fossil fuel electrical plant.
EXTERNAL COMBUSTION
Notes: Source: http://www.eoearth.org/view/article/152840/

## Slide 7
Notes: Source: http://bradleydibble.authorsxpress.com/tag/cooling-towers/

## Slide 8
Thermal efficiency, e represents the fraction of QH that is converted to useful work.
e = 1 – TC / TH < 1
This is the absolute max efficiency of a heat engine.

## Slide 9: Efficiency of various heat engines
Car engines 20% to 25%
Fossil fuel plants 20% to 40%
Diesel heat engines: 20% to 40%

## Slide 10
Hot Reservoir
QH
Engine
Surroundings
W
A heat engine can never be 100% efficient in converting heat into mechanical work.
Second Law of thermodynamic?
QC= 0

## Slide 11: Fuel engines
Chemical Potential Energy→ Thermal energy→ Kinetic energy
Regular fuel engines.
http://auto.howstuffworks.com/engine1.htm
http://www.youtube.com/watch?v=r96tepCk17w&feature=related

## Slide 12: Two strokes engine
http://science.howstuffworks.com/transport/engines-equipment/two-stroke2.htm
Lawnmowers
Garden equipment (chain saws, leaf blowers, trimmers)
Dirt bikes
Mopeds
Jet skis
Small outboard motors

## Slide 13
CAR ENGINE
INTERNAL COMBUSTION
The four–stroke OTTO cycle of a conventional petrol engine

## Slide 14
Notes: Source: http://www.grc.nasa.gov/WWW/k-12/airplane/otto.html

## Slide 15
5  1: inlet stroke volume increases as piston moves down creating a partial vacuum to aid air/fuel entering cylinder via the open inlet valve.
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Otto Cycle
adiabatic
isothermals

## Slide 16
1  2: compression stroke inlet valve closes piston moves up compressing the air/fuel mixture adiabatically.
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Otto Cycle
adiabatic
isothermals

## Slide 17
2  3: ignition – spark plug fires igniting mixture - constant volume combustion.
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Otto Cycle
adiabatic
isothermals

## Slide 18
3  4: expansion or power stroke – heated gas expands adiabatically as the piston is pushed down doing work
(Vmax = r Vmin). Compression ratio, r
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Otto Cycle
adiabatic
isothermals

## Slide 19
4  1 start of Exhaust stroke – outlet valve opens and mixture expelled at constant volume then 1  5
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Otto Cycle
adiabatic
isothermals

## Slide 20: Diesel engine
http://www.youtube.com/watch?v=1hamvuWLomc
Source: http://blog.caranddriver.com/2009-subaru-impreza-forester-diesel-car-news/
Notes: Source: http://blog.caranddriver.com/2009-subaru-impreza-forester-diesel-car-news/

## Slide 21
= = N∙m = Joule
The work done on a gas is the area under a PV curve.

## Slide 22
5
4
3
1
2
P
o
V
2
V
1
Q
H
Q
C
released to
surroundings
V
P
Diesel Cycle
adiabatic
isothermals

## Slide 23
Diesel engines
Harder to start (especially in cold temperatures)
More efficient than petrol engines (higher compression ratios).
No pre-ignition of fuel since no fuel in cylinder during most of the compression.
They need no ignition system, but the fuel-injection system requires expensive high-precision machining. (NO SPARK PLUG)

## Slide 24
Part 2: Combustions of Fuels

## Slide 25
The reason why fossil fuels are such a precious source of fuel is that a lot of energy can be produced from a relatively small amount of it.
The energy of the fuel source is stored within the bonds of the molecules as chemical potential energy.

## Slide 26
Notes: Source: http://expeditieaarde.blogspot.ca/2013_01_01_archive.html

## Slide 28
Biodiesel molecule from soya oil

## Slide 30
Carburant | Chaleur de combustion (kJ/mole) | Masse molaire (g/mole) | Chaleur de combustion massique (kJ/g)
Éthanol |  |  | 
Octane (essence) |  |  | 
Biodiésel | 11 113 | 294 | 37.8

## Slide 31
Carburant | Chaleur de combustion (kJ/mole) | Masse molaire (g/mole) | Chaleur de combustion massique (kJ/g)
Éthanol | 1261 | 46 | 27.4
Octane (essence) |  |  | 
Biodiésel | 11 113 | 294 | 37.8

## Slide 32
Carburant | Chaleur de combustion (kJ/g) | Masse volumique (g/mL) | Chaleur de combustion volumique (kJ/mL)
Éthanol | 27.4 | 0.79 | 21.6
Octane (essence) | 44.7 | 0.70 | 31.3
Biodiésel | 37.8 | 0.88 | 34.9
L’éthanol contient moins d’énergie par litre. Il faut donc un volume supplémentaire (en litres) pour parcourir la même distance avec un véhicule (environ 30% de plus).

## Slide 33
Par contre, même s’il faut plus d’éthanol (30% de plus environ) pour un rendement énergétique égale, l’éthanol produit UN PEU MOINS de dioxyde de carbone que l’octane.

## Slide 34
Type of fuel | Content required | Type of biofuel | Date of regulation
Fuel | 5% | Ethanol | December 15th 2010
Diesel and heating crude oil | 2% | Biodiesel | July 1st 2011 January 2013 (Québec et maritimes)

## Slide 35: 1350km on a tank? Look at the new TDI Passat http://web.vw.com/tdi-clean-diesel/

## Slide 36: Savais-tu?
For more info: http://www.mouvementcollectif.org/wp-content/uploads/2009/05/le-biodiesel-biobus-rapportfinal-lien1-fr.pdf